## Slide 1: Parallel Computer Architecture/Programming Models
Introduction to Parallel and Distributed Computing

## Slide 2: Learning Outcomes
Define parallelism in hardware and software.
List parallel computer architectures types
Explain different parallel computer architectures.

## Slide 3: Outline
Parallel architecture types
Instruction-level parallelism
Vector processing
Flynn’s Taxonomy
Shared memory
  Memory organization: UMA, NUMA
  Coherency: CC-UMA, CC-NUMA
Interconnection networks
Distributed memory
Clusters
Clusters of SMPs
Heterogeneous clusters of SMPs

## Slide 4: Parallelism and Parallel vs. Distributed
Parallel computing generally means:
  Vector processing of data
  Multiple CPUs in a single computer
Distributed computing generally means:
  Multiple CPUs across many computers

## Slide 5: Different Workers
Different threads in the same core
Different cores in the same CPU
Different CPUs in a multi-processor system
Different machines in a distributed system

## Slide 6: How do you get parallelism in the hardware?
Task Parallelism
  Distribute Instructions across processors
Data parallelism
  Distribute Instructions across processors
Instruction-Level Parallelism (ILP)
Bit-level parallelism
Processor parallelism
  Increase number of processors
Memory system parallelism
  Increase number of memory units
  Increase bandwidth to memory
Communication parallelism
  Increase amount of interconnection between elements
  Increase communication bandwidth

## Slide 7: Parallel Architecture Types
Uniprocessor
  Scalar processor
  Vector processor
  Data Parallel - Flynn’s Taxonomy (SISD, SIMD, MIMD)
processor
memory
processor
memory
vector
processor
memory
…

## Slide 8: Flynn’s Taxonomy
…

## Slide 9: Parallel Architecture Types
SPMD
Shared Memory Multiprocessor (SMP)
  Shared memory address space
  Bus-based memory system
  Interconnection network
processor
processor
memory
bus
processor
processor
memory
network
…
…
…

## Slide 10: Parallel Architecture Types
SPMD
In computing, single program, multiple data is a technique employed to achieve parallelism; it is a subcategory of MIMD
Shared Memory Multiprocessor (SMP)
  Shared memory address space
  Bus-based memory system
  Interconnection network
processor
processor
memory
bus
processor
processor
memory
network
…
…
…

## Slide 11: Parallel Architecture Types (2)
Distributed Memory Multiprocessor
  Message passing between nodes
  Massively Parallel Processor (MPP)
    Many, many processors
processor
memory
processor
memory
processor
memory
processor
memory
interconnection network
…
…

## Slide 12
Distributed-memory multiprocessor architecture.
In a distributed-memory multiprocessor, each memory module is associated with a processor as shown in below Fig. Any processor can directly access its own memory. A message passing (MP) mechanism is used in order to allow a processor to access other memory modules associated with other processors. Message passing interface (MPI) is a language-independent communication protocol.

## Slide 13: Parallel Architecture Types (2)
Cluster of SMPs
  Shared memory addressing within SMP node
  Message passing between SMP nodes
  Can also be regarded as MPP if processor number is large
…
…
…
…
…
…
interconnection network
M
M
M
M
P
P
P
P
P
P
P
P
network
interface

## Slide 14: Parallel Architecture Types (3)
Multicore
  Multicore processor
  GPU accelerator
  “Fused” processor accelerator
memory
C
C
C
C
m
m
m
m
processor
memory
PCI
processor
memory
cores can be hardware multithreaded (hyperthread)

## Slide 15: Parallel Architecture Types (3)
Multicore SMP+GPU Cluster
  Shared memory addressing within SMP node
  Message passing between SMP nodes
  GPU accelerators attached
…
…
…
…
…
…
interconnection network
M
M
M
M
P
P
P
P
P
P
P
P

## Slide 16: Instruction-Level Parallelism
Simultaneous execution of multiple instructions of a Program.
Opportunities for splitting up instruction processing
Pipelining within instruction
Pipelining between instructions
Overlapped execution
Multiple functional units
Out of order execution
Multi-issue execution
Superscalar processing
Hardware multithreading (hyperthreading)
Notes: Instruction Pipelining studied in OS - Oral Quiz.

## Slide 17: Parallelism in Single Processor Computers
CDC
6600
FPS
AP-120B
CDC
7600
CRAY-1
CDC
Cyber-205
only scalar
instructions
issue-when-
ready
register to register
memory to memory
horizontal
control
vector
instructions
Pipelined
Unpipelined
multiple
E unit
Vector
VLIW
IBM
360/91
ILP
scoreboarding
reservation stations
History of processor architecture innovation

## Slide 18: Home Task
Read about
  Bit-Level Parallelism

## Slide 19: Vector Processing
Scalar processing
  Processor instructions operate on scalar values
  integer registers and floating-point registers
Vectors
  Set of scalar data
  Vector registers
    integer, floating point (typically)
  Vector instructions operate on vector registers (SIMD)
Issues
  Vector unit pipelining
  Multiple vector units
  Vector chaining

## Slide 20: Next Class
Parallel Computer Architecture/Programming Models (Continued..)
  Architecture’s Classification according to Memory