## Slide 1: Parallel Computer Architecture/Programming Models
Introduction to Parallel and Distributed Computing

## Slide 2: Learning Outcomes
Classification according to Flynn’s Taxonomy
Classification according to Memory
  Shared Memory vs Distributed Memory

## Slide 3: Outline
Parallel architecture types
Instruction-level parallelism
Vector processing
Classification according to Flynn’s Taxonomy
Classification according to Memory
  Shared Memory vs Distributed Memory
Shared Memory
  Memory organization: UMA, NUMA
  Coherency: CC-UMA, CC-NUMA
Interconnection networks
Distributed memory
Clusters
Clusters of SMPs
Heterogeneous clusters of SMPs

## Slide 4: Flynn’s Taxonomy and Data Parallelism
Instructions
Single (SI)
Multiple (MI)
Data
Multiple (MD)
SISD Single-threaded process | MISD Pipeline architecture
SIMD Vector Processing | MIMD Multi-threaded Programming
Single (SD)
One of the more widely used parallel computer classifications, since 1966, is called Flynn’s Taxonomy
It distinguishes multiprocessor computers according to the dimensions of Instruction and Data
SISD: Single instruction stream, Single data stream
SIMD: Single instruction stream, Multiple data streams
MISD: Multiple instruction streams, Single data stream
MIMD: Multiple instruction streams, Multiple data streams

## Slide 5: SISD Machines
A serial (non-parallel) computer
Single instruction: Only one instruction stream is acted on by CPU during any one clock cycle
Single data: Only one data stream is used as input during any one clock cycle
Deterministic execution
Oldest and most prevalent form computer
Examples: Most PCs, single CPU
workstations and mainframes
D
D
D
D
D
D
D
Processor
Instructions

## Slide 6: SIMD Machines (I)
A type of parallel computers
Single instruction: All processor units execute the same instruction at any give clock cycle
Multiple data: Each processing unit can operate on a different data element
It typically has an instruction dispatcher, a very high-bandwidth internal network, and a very large array of very small-capacity instruction units
Best suitable for specialized problems e.g., image processing
Two varieties: Processor Arrays and Vector Pipelines
Examples: Connection Machines, MasPar-1, MasPar-2;  IBM 9000, Cray C90, Fujitsu VP, etc

## Slide 7: SIMD Machines (II)

## Slide 8: SIMD Machines (III)

## Slide 9: MISD Machines (I)
A single data stream is fed into multiple processing units
Each processing unit operates on the data independently via independent instruction streams
Very few actual machines: CMU’s C.mmp computer (1971)
Possible use: multiple frequency filters operating on a single signal stream

## Slide 10: MISD Machines (II)

## Slide 11: MIMD Machines (I)
Multiple instruction: Every processor may execute a different instruction stream
Multiple data: Every processor may work with a different data stream
Execution can be synchronous or asynchronous, deterministic or nondeterministic
Examples: most current supercomputers, grids, networked parallel computers, multiprocessor SMP computer

## Slide 12: MIMD Machines (II)

## Slide 13: Parallel vs. Distributed
Shared
Memory
Parallel: Multiple CPUs within a shared memory machine
Distributed: Multiple machines with own memory connected over a network
Network connection for data transfer
D
D
D
D
D
D
D
Processor
Instructions
D
D
D
D
D
D
D
Processor
Instructions

## Slide 14: Data Parallel Architectures
Array of simple processors with memory
Processors arranged in a regular topology
Control processor issues instructions
Specialized synchronization and communication
Specialized reduction operations
Array processing

## Slide 15: Next Class
Parallel Computer Architecture/Programming Models (Continued..)
  Memory